## Slide 1: Basmati · بصمتي
GRADUATION PROJECT PROPOSAL
Daily carbon footprint for people and a government facility: a phone app and an IoT energy monitor, piloted on the Computer Science department floor
6.8 kg
daily budget
TEAM
[9 team members]
SUPERVISOR
[Supervisor name]
PILOT SITE
CS department floor
DATE
October 2026
Notes: Introduce the project in one sentence: an Android app that calculates each person’s carbon footprint every day with almost no typing, plus IoT monitors that measure the electricity of a government facility. The pilot is the Computer Science department floor: its members use the app, and the floor itself gets a daily footprint and a waste report for the department head.

## Slide 2: Nobody sees the footprint of a person or of a public building
THE PROBLEM
No idea of size or source
Neither people nor facility managers know how much CO₂e they produce, or which habit or room produces most of it.
One bill, too late
A government building gets one monthly bill for the whole building: no floor, no hour, no person, and it arrives after the energy is used.
Not built for Egypt
Personal calculators are yearly questionnaires with foreign factors: no microbus, no koshary, no Egyptian grid.
Goal: measure the CS floor and each member’s day automatically, with Egyptian factors and real data, and show where the waste is.
Notes: Evidence: in Cairo’s public administrative buildings about 40% of electricity goes to cooling and 60% to lighting and equipment [24]; Egyptian university buildings usually lack monthly per-building data [23]; universities that do measure their footprint do it once a year [1, 22]; and a review of ten personal calculators found inconsistent, opaque results [29].

## Slide 3: Egypt is below the world average, but above the 2030 target
CARBON FOOTPRINT
A carbon footprint is the total greenhouse gas caused by a person, product or building over a period, measured in kg of CO₂-equivalent (CO₂e).
Every activity converts to CO₂e through an emission factor: kWh of electricity, km travelled, kg of food.
DAILY BUDGET PER PERSON
2,500 kg ÷ 365 ≈ 6.8 kg CO₂e
3.4 t
per person per year in Egypt (2023)
6.6 t
world average per person (2023)
2.5 t
1.5 °C lifestyle target per person by 2030
Sources: EDGAR 2024 report [27]; Hot or Cool Institute, 1.5-Degree Lifestyles [26]
Notes: The 6.8 kg daily budget is the 2030 target divided by 365 days. The app colors a person’s day green up to 4.8 kg (70%), yellow up to 6.8 kg and red above it. Country figures are territorial emissions; the target is a lifestyle (consumption) figure, so the comparison is indicative.

## Slide 4: One app and one floor monitor, two daily numbers
OUR SOLUTION
Transport
Commute detected from GPS and motion sensors; one tap to confirm when unsure
Food
Photo of the plate, at the cafeteria or at home; the model names the dish
Floor electricity
ESP32 monitors on the floor’s electrical board; each person gets a share for their hours there
Facility dashboard
Daily kWh, CO₂e, after-hours waste and a forecast for the department head
Every night: each person’s day against a 6.8 kg budget in the app, and the floor’s day against its own baseline on a display at the floor entrance, in green, yellow or red.
Notes: Pilot site: the Computer Science department floor, a government facility. Example: “Today you produced 6.4 kg out of 6.8; your biggest item was food.” and “The floor used 330 kWh (149 kg CO2e); 40 kWh were used after hours in Lab 3.” Out of scope: other floors, purchases, flights (manual entry only), iOS, and switching devices on or off: we measure and alert, we do not control.

## Slide 5: The phone and the floor monitors feed one server
SYSTEM ARCHITECTURE
INPUTS
Trip tracking
GPS + transport model on phone
Food camera
meal model on phone (LiteRT)
Floor check-in
geofence: hours on the floor
Floor monitors
2 × ESP32 + CT clamps on the board
SERVER · FASTAPI
Trip and meal API
REST, from the phone
Energy ingest
MQTT · Mosquitto
Daily footprint engine
personal and floor totals
Forecast and waste
LightGBM + after-hours rules
Database
PostgreSQL + TimescaleDB
OUTPUTS
Personal summary
total, items, color in the app
Entrance display
LED ring: the floor’s day
Facility dashboard
for the department head
Waste alerts
to the floor technician
Notes: The models run on the phone, so photos and locations never leave it: the server receives only final numbers such as distance, mode, dish, portion and hours on the floor. Monitor A measures the three main phases of the floor; monitor B measures three chosen circuits (lab ACs, lab PCs, lighting). The server can run on a faculty server or a free cloud tier.

## Slide 6: The app senses, the user confirms, the server adds up
WORKFLOW
1
Sense
2
Classify
3 · USER
Confirm
4
Compute
5
Notify
6
Improve
When | What happens
A trip ends | Mode classified on the phone; one-tap question if confidence is below 70%
A meal photo is taken | Top 3 dishes shown; the user picks the dish and the size
Arriving at the department | Geofence check-in counts the hours on the floor (no location is kept)
Every 10 seconds | Floor monitors send current per phase and per circuit
After working hours | Load above the base level outside the timetable raises a waste alert
11 pm | Personal total and color in the app; the floor’s total and color on the entrance display
Every week | A personal tip; a floor report to the department head
Notes: Step 6 means every user answer becomes new training data: a confirmed trip mode, a corrected dish or a confirmed waste alert improves the next model version.

## Slide 7: Three pipelines, two daily numbers
DATA FLOW
Transport
GPS and motion sensors
Trip segments
Mode classifier
Trip record
GPS points and sensor windows → trips → mode and km on the phone → record sent by REST (raw GPS stays on the phone)
Food
Plate photo
MobileNet on phone
Top 3 + size
Meal record
photo → 224 × 224 image → dish probabilities → user picks dish and portion → record (the photo stays on the phone)
Energy
CT clamps on the floor board
MQTT every 10 s
TimescaleDB
kWh, forecast, waste
current samples → Irms per phase, W, Wh → JSON message → time-series table → daily kWh, forecast and after-hours waste
Daily footprint engine
+ hours on the floor, timetable, home bill
App, entrance display, dashboard, alerts
Notes: Each pipeline sends small records, not raw media. The phone sends one record per trip and per meal and the hours spent on the floor each day; the floor monitors report every 10 seconds. The timetable comes from the department once per term, and the optional home part comes from the monthly bill.

## Slide 8: What travels between the components
DATA FLOW · RECORDS
Record | Key fields | Rate | Stored in
Meter reading | device, circuit, time, Irms, W, Wh | every 10 s | TimescaleDB
Trip record | user, start, end, km, mode, confidence, passengers | per trip | PostgreSQL
Meal log | user, dish, portion, time | per meal | PostgreSQL
Floor presence | user, date, hours on the floor | daily | PostgreSQL
Timetable | room, day, hour, expected people | per term | PostgreSQL
Waste event | circuit, start, end, kWh, confirmed | when found | PostgreSQL
Daily footprint | user or floor, date, items, total, color | daily | PostgreSQL
Privacy by design: photos and locations never leave the phone, presence is stored as hours only, volunteers are IDs instead of names, and raw GPS is deleted once the trip is summarized.
Notes: Fixing these record formats in week 2 lets every team work in parallel with mock data. Emission factors live in one settings file on the server, so a factor can be updated without changing code.

## Slide 9: Every footprint is activity × emission factor
EQUATION 1 · THE CORE RULE
Ai is the amount of activity i (kWh, km, kg) and EFi its emission factor in kg CO₂e per unit.
PERSONAL BUDGET = 2,500 kg ÷ 365 ≈ 6.8 kg
Green
≤ 4.8 kg (70%)
Yellow
≤ 6.8 kg
Red
> 6.8 kg
Activity | Unit | kg CO₂e / unit
Egypt grid electricity (2024) | kWh | 0.45
Petrol car, ÷ passengers | km | 0.17
Microbus or bus | passenger-km | 0.10
Metro | passenger-km | 0.06
Walking or cycling | km | 0
LPG cylinder (12.5 kg) | cylinder | 37.5
Beef (dairy to beef herd) | kg | 33 to 99.5
Chicken | kg | 9.9
Rice | kg | 4.5
Lentils and beans | kg | 1.8
Notes: Sources: grid factor from Low-Carbon Power (447 g per kWh in 2024); food from Poore and Nemecek (2018); transport and LPG values are approximate, based on UK DESNZ factors and standard LPG combustion. Microbus and metro values are our estimates and will be documented in the report.

## Slide 10: One person’s daily footprint D, in kg CO₂e
EQUATION 2 · A PERSON’S DAY
d trip distance (km); fmode mode factor
fdish meal footprint; s portion 0.7, 1 or 1.4
Efloor floor kWh per day from the monitors
hi your hours on the floor; H all person-hours
Ehome home kWh per day from the monthly bill (optional)
G home gas: cylinders × 37.5 ÷ 30; Nhome members
Transport
2.0
Food
2.6
Floor share
0.6
Home
1.2
Example day total
6.4 kg · 94% · yellow
Notes: Example day for a student: 20 km by microbus (2.0); beans, two eggs, rice and 150 g of chicken (2.6); 6 hours on a floor that used 330 kWh with 1,480 person-hours: 0.45 × 330 × 6 ÷ 1,480 = 0.6; a share of a home that uses 250 kWh a month with 4 members plus one gas cylinder a month (0.9 + 0.3 = 1.2). Total 6.4 kg: under the 6.8 kg budget but above the 4.8 kg green line, so the day shows yellow. Swapping the chicken for 150 g of beef raises the day to about 9.9 kg, which is red.

## Slide 11: A meal’s footprint comes from its ingredients
EQUATION 3 · MEALS
w j = raw weight of ingredient j in kg · EF j = its factor (Poore and Nemecek) · s = portion size chosen by the user
Dish (medium plate) | Ingredients, raw weight | kg CO₂e
Koshary | rice 100 g, lentils 50, pasta 50, tomato 50, onion 30 | 0.73
Chicken with rice | chicken 150 g, rice 100 | 1.93
Beef with rice | beef 150 g, rice 100 | 5.4 to 15.4
The team builds this table for 20 dishes, including the faculty cafeteria menu. Beef uses the dairy-herd factor (33) as a conservative value.
Notes: The beef range comes from the two Poore and Nemecek factors: 33 kg CO2e per kg for beef from dairy herds and 99.5 for beef herds. Recipes come from three sources per dish plus weighing a real plate on a kitchen scale.

## Slide 12: The floor’s footprint, intensity and after-hours waste
EQUATION 4 · THE FLOOR
Efloor floor kWh per day, all three phases
I kg CO₂e per person-hour; H person-hours from the timetable
Ebase same weekday, first 3 weeks (before feedback)
Twork timetable hours; Pbase night base load (servers, fridges)
Green
r ≤ 0.9
Yellow
r ≤ 1.0
Red
r > 1.0
Example: 330 kWh → 149 kg CO₂e, 0.10 kg per person-hour; 40 kWh after hours = 18 kg wasted.
Notes: The floor gets its own color against its own baseline, so improvement is visible even though a floor is much larger than a person: green means at least 10% below the baseline day. The waste term counts only energy above the night base load outside timetable hours, for example lab ACs left running after 6 pm.

## Slide 13: From current samples to calibrated kWh on three phases
EQUATION 5 · ENERGY MONITOR
1
Monitor A: a clamp on each of the floor’s three main phases.
2
Monitor B: clamps on lab ACs, lab PCs and lighting.
3
Power uses V = 220 V and k, updated weekly from a reference reading.
4
Target: weekly error below 10%.
Notes: Clamps close around the cables without cutting them: 100 A clamps (SCT-013-100 with a burden resistor) on the main phases and 30 A clamps on circuits. The ADS1115 samples the clamps (up to 860 samples per second in total). The faculty electrician installs the monitors with the board switched off, under an official approval; the devices run on 5 V adapters, so no mains voltage enters their circuits. The reference reading is the floor sub-meter if there is one, otherwise a handheld power meter from the electrical lab.

## Slide 14: Four core models and one optional
AI MODELS
Model | Input | Method | Runs on | Priority
Transport mode | Speed, stops, acceleration, sensor vibration, GPS loss | Activity Recognition API, then Random Forest or LightGBM | Phone | Core
Meal recognition | Plate photo | Transfer learning on MobileNetV3 or EfficientNet-Lite0, LiteRT int8 | Phone | Core
Floor forecast | Hourly kWh, hour, weekday, temperature, timetable | LightGBM; LSTM if there is enough data | Server | Core
After-hours waste | Load per circuit, timetable, forecast | Rules first, then Isolation Forest on forecast errors | Server | Core
Appliance breakdown (NILM) | Floor main power | Disaggregation, checked against monitor B | Server | Optional
Rule: every model must beat a simple baseline measured first, on people and days not used in training.
Notes: Baselines: the Activity Recognition API alone for transport, the most common dish for meals, the same hour last week for the floor forecast, and a fixed threshold for waste. Metro trips are found by a rule: GPS is lost underground and the trip starts and ends inside a geofence around a station. The Random Forest is exported to Kotlin code with m2cgen, so it runs without an ML library.

## Slide 15: Public data for pretraining and benchmarks
DATASETS · PUBLIC
Dataset | Year | Contents | Our use
ImageNet | 2012 | About 1.28M training images, 1,000 classes | Pretrained MobileNetV3 weights
Food-101 | 2014 | 101,000 images of 101 dishes | Food pretraining and benchmark
SHL | 2018 | Phone sensor data, 8 transport and locomotion modes | Pretrain the transport classifier
GeoLife | 2012 | GPS trajectories from 182 users, part with mode labels | Benchmark trip features
Building Data Genome 2 | 2020 | Hourly meters of 1,636 non-residential buildings, 2 years | Pretrain and benchmark the forecast
UK-DALE | 2015 | Whole-house and appliance demand, 5 UK homes | NILM benchmark (optional)
Poore and Nemecek | 2018 | Global food life-cycle emission factors | Dish footprints
OpenStreetMap | — | Locations of Cairo metro stations | Metro geofences
Open-Meteo | — | Hourly temperature at the faculty | Forecast input
Notes: Public datasets do not contain microbuses, Egyptian dishes or Egyptian public buildings, so they are used for pretraining and benchmarking only. Building Data Genome 2 is the dataset of the ASHRAE competition [37] and includes many university buildings. The final evaluation is always on the data we collect ourselves.

## Slide 16: Egyptian data, collected with consent and approval
DATASETS · COLLECTED BY THE TEAM
Data | Amount | How | Weeks
Floor electricity | 6 channels every 10 s; about 2,350 hourly readings each | Monitors on the floor board; weekly reference reading | 6–20
Timetable and presence | Room schedule; hours on the floor per volunteer | Department administration; app check-in | 2–20
Building bills | 12–24 months of the building’s electricity bills | Official request to the faculty administration | 2–4
Food photos | 200+ per dish: 3,000 photos from 30 people | Volunteers photograph meals and pick the dish name | 4–10
Labeled trips | 20 volunteers × 2 weeks ≈ 560 trips; 80+ per mode | Volunteer mode records GPS and sensors; user picks the mode | 5–9
Waste events | About 30 labeled after-hours events | Staged with the technician, plus confirmed alerts | 8–18
Split 70 / 15 / 15 by person and by week, never by photo or hour, so tests reflect new people and new days.
Consent forms, IDs instead of names, raw GPS deleted after feature extraction, right to withdraw.
Notes: Also collected: recipes for 20 dishes (three sources each plus a weighed plate) and the metro stations from OpenStreetMap. Staged waste events are done with the floor technician, for example leaving one lab AC on for an hour after the last lecture, so the true start and end are known. Collecting this Egyptian data is what makes the project stand out at the defense.

## Slide 17: How each kind of model is measured
PERFORMANCE METRICS
Classification
transport mode per trip; waste events found or missed
Regression
floor forecast, monitor error, trip distance
Top-k accuracy
meal recognition: is the true dish in the model’s k best guesses?
Notes: TP, FP, FN: true positives, false positives, false negatives. For transport they are computed per mode and averaged (macro F1); for waste a detection counts as correct if it overlaps a labeled event. For the meal model we report Top-1 and Top-3, because the app shows the three best guesses. MAPE is used for the daily floor forecast; MAE and RMSE for distance and monitor error.

## Slide 18: What “working” means for each part
PERFORMANCE TARGETS
Part | Metric | Target
Transport mode | Accuracy per trip | At least 85%
Trip distance | Error vs. true distance | Below 10%
Meal recognition | Top-1 / Top-3 accuracy | At least 80% / 95%
Meal speed | Time on a mid-range phone | Under 1 second
Floor monitor | Weekly error vs. reference reading | Below 10%
Floor forecast | Daily MAPE | Below 15%, and beats last week
Waste detection | Recall / precision on labeled events | At least 90% / 80%
Battery | App use per day | Below 5%
Real data | Volunteers and site | 20 volunteers, 1 floor, 14 weeks
Notes: All targets are measured on people and days that were not used for training. We report the real numbers even if they fall short of the target.

## Slide 19: The four curves we will report
CURVES
Training vs. validation loss
Meal model, by epoch. A growing gap between the lines means overfitting.
Confusion matrix
Transport modes: walk, microbus, car, metro. Shows which modes get mixed up.
Monitor vs. reference
Weekly floor kWh from our monitor beside the reference reading. The gap is the monitor error.
Predicted vs. actual kWh
One working day on the floor, hour by hour. The gap is what MAPE measures.
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
Training | 1.72 | 1.43 | 1.193 | 0.998 | 0.839 | 0.709 | 0.602 | 0.515 | 0.443 | 0.384 | 0.337 | 0.297 | 0.265 | 0.239 | 0.217 | 0.2 | 0.185 | 0.173 | 0.164 | 0.156
Validation | 1.81 | 1.524 | 1.294 | 1.109 | 0.961 | 0.843 | 0.747 | 0.671 | 0.609 | 0.56 | 0.533 | 0.513 | 0.499 | 0.491 | 0.487 | 0.485 | 0.487 | 0.49 | 0.496 | 0.502
 | Walk | Micro | Car | Metro
Walk |  |  |  | 
Micro |  |  |  | 
Car |  |  |  | 
Metro |  |  |  | 
rows: true mode · columns: predicted
Chart: 
| W1 | W2 | W3 | W4 | W5 | W6 | W7 | W8
Monitor | 1738 | 1651 | 1901 | 1751 | 1810 | 2090 | 1911 | 1833
Reference | 1640 | 1720 | 1810 | 1700 | 1905 | 2010 | 1950 | 1780
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23
Measured | 5 | 5 | 5 | 5 | 5 | 5 | 6 | 9 | 16 | 22 | 25 | 27 | 28 | 27 | 26 | 24 | 19 | 14 | 10 | 8 | 7 | 6 | 5 | 5
Forecast | 5 | 5.39 | 5.21 | 4.72 | 4.65 | 5.09 | 6.48 | 9.23 | 14.94 | 20.66 | 25.84 | 29.13 | 28.24 | 24.99 | 24.74 | 25.16 | 20.41 | 13.88 | 9.21 | 7.73 | 7.43 | 6.4 | 4.87 | 4.6
Illustrative shapes only, not results. The real curves come from our test data in weeks 10 and 18.
Notes: These are the plots that will appear in the results chapter. They are sketches of the expected shape, not results. Each curve is produced from the held-out test data at the first-version review (week 10) and in the final evaluation (week 18).

## Slide 20: Universities and schools measure their footprint in three scopes
MEASURING AN EDUCATIONAL INSTITUTION
SCOPE 1 · DIRECT
Fuel burned on site
Gas for heating and kitchens, diesel generators, the institution’s buses, refrigerant leaks
Basmati: Optional manual entry
SCOPE 2 · ELECTRICITY
Purchased electricity
Labs, PCs, air conditioning and lighting
Basmati: Measured every 10 s by the floor monitors
SCOPE 3 · VALUE CHAIN
Everything else
Student and staff commuting, food, purchases, waste, water, business travel
Basmati: Commuting and meals per person, from the app
Standards: GHG Protocol Corporate and Scope 3 Standards; ISO 14064-1:2018; ISO/TR 14069. Emissions = activity × emission factor, then normalized per person or per m².
Notes: Almost every campus study uses these three scopes from the GHG Protocol [1, 10, 14, 18, 22]; some also follow ISO 14064-1 and ISO/TR 14069 [14, 16]. Our project measures Scope 2 directly and the largest part of Scope 3 (commuting and food) per person, which the literature identifies as the biggest and most uncertain part of a campus inventory [13, 14, 19, 22]. The UI GreenMetric ranking also uses the total carbon footprint divided by the campus population as an indicator.

## Slide 21: How to measure the footprint of a university
RELATED WORK 2020–2026 · 1 OF 5
Paper | Year | What we take from it
[1] Valls-Val and Bovea — Carbon footprint in higher education institutions: a literature review | 2021 | Scopes, methods and sources used by universities
[3] Helmers, Chang and Dauwels — Carbon footprinting of universities worldwide, Part I | 2021 | 20 universities; standardized metrics needed to compare
[4] Valls-Val and Bovea — CO2UNV: a carbon footprint tool for universities | 2022 | Scopes 1–3 per university or per building
[6] Herth and Blok — Universities’ direct and indirect emissions (TU Delft) | 2023 | 106 kt, 80% Scope 3; spending-based estimates are weak
[7] Kiehle et al. — Carbon footprint of the University of Oulu | 2023 | Hybrid input-output and LCA; heating is the largest item
[9] Abdelbasier et al. — Monitoring and mitigation in higher education (Ain Shams Univ. journal) | 2022 | Egyptian review; electricity is a major share
Numbers in brackets match the references at the end of the deck, with DOIs and links.
Notes: These papers define how a university footprint is measured: the GHG Protocol scopes, the list of sources, and the choice between measuring activities and estimating from spending. Also relevant: a bibliometric analysis of 283 papers on the topic [2], a standardized tool applied to all Spanish universities [5], and a 2025 integrated assessment model [8].

## Slide 22: Measured campuses: commuting and buildings dominate
RELATED WORK 2020–2026 · 2 OF 5
Institution | Country | Year | t CO₂e | Per person | Largest source | Ref.
Clemson University | USA | 2014–17 | ≈ 95,400 | — | Electricity and Scope 3, ≈ 40% each | [11]
Univ. Nacional de Colombia | Colombia | 2019 | 7,251 | 0.43 t | Transport 58.5%; Scope 3 83% | [14]
NED University | Pakistan | 2017 | ≈ 21,500 | 1.79 t | Scope 3 85.6% | [13]
TU Delft | Netherlands | 2018 | ≈ 106,000 | — | Scope 3 ≈ 80% (purchases) | [6]
University of Oulu | Finland | 2019 | 19,072 | — | District heating | [7]
University of Bologna | Italy | 2020 | 16,467 | — | IT purchases ≈ 50% (transport 74% in 2018) | [16]
TU Cluj-Napoca | Romania | 2023 | 7,229 | 0.36 t | Natural gas for heating | [18]
Sichuan Univ. Jinjiang College | China | 2023 | 44,584 | 1.89 t | Electricity | [19]
Port Said University, Faculty of Science | Egypt | 2023–24 | — | — | Scope 3 (commuting) ≈ 97% | [22]
Boundaries and years differ, so totals are not directly comparable; per-person figures are the fairer comparison.
Notes: Two patterns matter for us. First, Scope 3, mainly commuting, is usually the largest part (80–97%), so the app measures every volunteer’s commute automatically. Second, where commuting is not counted or heating is by gas, building energy dominates; in Egypt that energy is mostly cooling [24]. The Sichuan study also shows that commuting and business travel are the most uncertain items [19]. The COVID-19 studies show how fast the mix changes when people stay home [12, 16].

## Slide 23: Schools, Egypt and continuous measurement
RELATED WORK 2020–2026 · 3 OF 5
Paper | Year | What we take from it
[20] Wagner et al. — Student-led carbon footprint assessment in schools (Schools4Future, Germany) | 2021 | Students measure their school: mobility, heating, electricity, canteen
[21] Adhikari and Pokhrel — Carbon footprint of schools in Pokhara, Nepal | 2025 | 8 schools, GHG Protocol; school buses are the largest item
[22] Badr, El Beheary and Hassan — Carbon footprint of Egyptian universities: Port Said University | 2026 | Egyptian government university, per faculty; commuting ≈ 97%
[23] Safwat et al. — Energy data for higher-education buildings in Egypt | 2024 | Monthly data per building often missing
[24] Hamada, Hong and Raslan — Cairo’s public administrative buildings | 2025 | About 40% cooling, 60% lighting and equipment
[25] García-Monge et al. — IoT monitoring on a smart campus in Spain | 2023 | Continuous measurement; 40–70% HVAC savings possible
Numbers in brackets match the references at the end of the deck, with DOIs and links.
Notes: Schools use the same GHG Protocol with simpler data [20, 21]. The Port Said study is the closest to ours: an Egyptian government university measured per faculty, where commuting dominates [22]. Egyptian buildings lack fine-grained data [23, 24], and continuous IoT measurement on a campus pays off [25]. Institutional reports also exist: the American University in Cairo has published footprint reports since 2012, Qatar University since 2016, and Alexandria University submits its footprint to UI GreenMetric.

## Slide 24: Personal footprint apps, transport and food
RELATED WORK 2020–2026 · 4 OF 5
Paper | Year | What we take from it
[28] Ajufo and Bekaroo — TCTracker: an automated personal carbon footprint calculator for transport | 2021 | GPS + AI app; tested with 40 users
[29] Bekaroo et al. — Calculating carbon emissions from personal travelling: key calculators | 2021 | 10 calculators: inconsistent and opaque
[30] Zhang et al. — SpeedTransformer for transport mode, tested in the CarbonClever app | 2026 | 348 users tracked for personal footprints
[31] Sadeghian, Håkansson and Zhao — Transport mode detection from GPS: a review | 2021 | Labeled trips are the bottleneck
[33] Wang and Jiang — T2Trans: temporal convolutional network on phone sensors | 2022 | Macro F1 86.42% on SHL, 8 modes
[34] Tahir and Loo — Survey of image-based food recognition and volume estimation | 2021 | Deep CNN features; mobile food logging
Numbers in brackets match the references at the end of the deck, with DOIs and links.
Notes: These papers support the personal part of the app: automatic commute tracking and meal recognition. Also used: the three-year SHL challenge review [32] and a systematic review of food recognition for dietary assessment [35]. The 2.5 t target [26] and the EDGAR country data [27] give the daily budget.

## Slide 25: Energy monitoring, forecasting and waste detection
RELATED WORK 2020–2026 · 5 OF 5
Paper | Year | What we take from it
[36] Ismail and Sahari — Real-time energy monitoring with ESP32 + SCT-013 | 2024 | Worst-case error ≈ 12.4%, so we calibrate weekly
[37] Miller et al. — ASHRAE Great Energy Predictor III: overview and results | 2020 | Gradient boosting (LightGBM) wins
[38] Anand et al. — Occupancy-based energy modelling for institutional buildings | 2021 | Occupancy matters; gradient boosting is fast
[39] Himeur et al. — AI-based anomaly detection of energy use in buildings: a review | 2021 | Methods for finding waste
[40] Azad, Rajabi and Estebsari — NILM with deep neural networks: a review | 2023 | Optional appliance breakdown
Numbers in brackets match the references at the end of the deck, with DOIs and links.
Notes: The 2024 ESP32 monitor is the closest hardware to ours, so we calibrate weekly. The ASHRAE competition and the institutional-buildings study are why we forecast with LightGBM and the timetable. The anomaly-detection review guides the waste detector.

## Slide 26: Campuses measure their footprint once a year from bills and surveys; nothing measures a public building and its people every day.
RESEARCH GAP
Daily, not yearly
Scope 2 measured every 10 s and commuting measured per trip, instead of one yearly inventory and a commuting survey.
Local factors and data
Microbus, metro, Egyptian dishes and the Egyptian grid, with data we collect ourselves.
Per person and per floor
Each person’s real share of the floor, plus after-hours waste alerts for the department head.
Notes: The literature measures educational institutions with the GHG Protocol, but once a year, for the whole campus, with commuting from surveys [1, 10, 14, 18, 22]. Our contribution applies the same scopes continuously, to one floor of a government building and to each of its people, with Egyptian factors.

## Slide 27: A full day computed automatically by week 10
TIMELINE · 20 WEEKS
Week 2
Interfaces and floor survey
MQTT, API, model inputs; rooms, labs, ACs and the board
Week 6
Monitors and volunteers
2 monitors on the floor board; volunteer app with 20 people
Week 10
First full version
A whole day computed end to end with the first models
Week 16
Feature freeze
No new features; fixing and measuring only
Week 20
Final delivery
Final numbers, demo and report draft
Weeks 1–10 · build
Interfaces, screens and database
Floor survey, official approval, installation in week 6
Trip tracking, food camera, daily screen
Volunteer mode and data collection
Weeks 13–20 · improve and measure
Improve the models; run them on the phone
Floor forecast, waste alerts and dashboard
Battery tests and final evaluation
Report, demo and defense
Weeks 11–12 are kept light for mid-year exams.
Notes: Weeks 11 and 12 are kept light for mid-year exams, assuming the project starts in early November 2026. The floor monitors keep recording during the exams and the break, which gives useful low-occupancy days for the baseline and the waste detector.

## Slide 28: Nine students, four teams, about 8,100 EGP
TEAM AND BUDGET
Team | People | Owns
Mobile app | 3 | Trip tracking; food camera and on-phone models; screens, check-in and volunteer mode
AI | 2 | Meal model and dish database; transport model; waste detection
Backend | 2 | API, database, daily calculation, MQTT, forecast, dashboard
Hardware | 2 | Circuits and enclosures; installation with the faculty electrician; calibration; entrance display
Server on a faculty server or a free cloud tier (0 EGP). Prices are estimates at the time of writing.
ESTIMATED BUDGET
8,140 EGP
Chart: 
| Monitors 5,500 | Printing 1,000 | Contingency 740 | Display 600 | Scale 300
Budget | 5500 | 1000 | 740 | 600 | 300
Notes: Monitors: 3 ESP32 boards, 7 CT clamps (six plus a spare) and 3 ADS1115 converters, with DIN-rail enclosures, burden resistors and 5 V adapters. Display: an LED ring in a small enclosure at the floor entrance. Contingency is 10%. The reference power meter is borrowed from the electrical lab. Extra roles: a team lead, a volunteer coordinator and a report editor.

## Slide 29: What we need to start week 1
NEXT STEPS
Decisions we need from you
Approval of the idea and the pilot on the CS floor
An official letter to the faculty administration for installation
Access to the timetable and past electricity bills
Consent form for 20 volunteers
Final team names and roles
Our next two weeks
Interfaces: MQTT, API and model inputs
Floor survey: rooms, labs, ACs, PCs and the board
Order parts; test one clamp on a kettle in the lab
Dish list with the cafeteria menu; consent form
Notes: The official approval and access to the floor’s electrical board are the items that can delay the project, so we ask for them first.

## Slide 30: Measuring universities: reviews, methods and tools
REFERENCES · 1 OF 5
[1] Valls-Val, K., & Bovea, M. D. (2021). Carbon footprint in higher education institutions: a literature review and prospects for future research. Clean Technologies and Environmental Policy, 23, 2523–2542. doi:10.1007/s10098-021-02180-2
[2] Li, Z., Chen, Z., Yang, N., Wei, K., Ling, Z., Liu, Q., Chen, G., & Ye, B. H. (2021). Trends in research on the carbon footprint of higher education: a bibliometric analysis (2010–2019). Journal of Cleaner Production, 289, 125642. doi:10.1016/j.jclepro.2020.125642
[3] Helmers, E., Chang, C. C., & Dauwels, J. (2021). Carbon footprinting of universities worldwide: Part I—objective comparison by standardized metrics. Environmental Sciences Europe, 33, 30. doi:10.1186/s12302-021-00454-6
[4] Valls-Val, K., & Bovea, M. D. (2022). Carbon footprint assessment tool for universities: CO2UNV. Sustainable Production and Consumption, 29, 791–804. doi:10.1016/j.spc.2021.11.020
[5] Guerrero-Lucendo, A., García-Orenes, F., Navarro-Pedreño, J., & Alba-Hidalgo, D. (2022). General mapping of the environmental performance in climate change mitigation of Spanish universities through a standardized carbon footprint calculation tool. International Journal of Environmental Research and Public Health, 19(17), 10964. doi:10.3390/ijerph191710964
[6] Herth, A., & Blok, K. (2023). Quantifying universities’ direct and indirect carbon emissions: the case of Delft University of Technology. International Journal of Sustainability in Higher Education, 24(9). doi:10.1108/IJSHE-04-2022-0121
[7] Kiehle, J., Kopsakangas-Savolainen, M., Hilli, M., & Pongrácz, E. (2023). Carbon footprint at institutions of higher education: the case of the University of Oulu. Journal of Environmental Management, 329, 117056. doi:10.1016/j.jenvman.2022.117056
[8] Deda, D., Gervásio, H., & Quina, M. J. (2025). Advancing carbon footprint in higher education: an integrated assessment model. The International Journal of Life Cycle Assessment. doi:10.1007/s11367-025-02514-y
Notes: References 1 to 9 are reviews, methods and tools for measuring the footprint of universities.

## Slide 31: Methods and measured universities
REFERENCES · 2 OF 5
[9] Abdelbasier, A. M., Kamel, M. M., Donia, N. S., & Nawar, H. A. (2022). Carbon footprint monitoring and mitigation in higher education: a meta-analysis review. Journal of Environmental Sciences (Ain Shams University), 51(11).
[10] Yañez, P., Sinha, A., & Vásquez, M. (2020). Carbon footprint estimation in a university campus: evaluation and insights. Sustainability, 12(1), 181. doi:10.3390/su12010181
[11] Clabeaux, R., Carbajales-Dale, M., Ladner, D., & Walker, T. (2020). Assessing the carbon footprint of a university campus using a life cycle assessment approach. Journal of Cleaner Production, 273, 122600. doi:10.1016/j.jclepro.2020.122600
[12] Filimonau, V., Archer, D., Bellamy, L., Smith, N., & Wintrip, R. (2021). The carbon footprint of a UK University during the COVID-19 lockdown. Science of the Total Environment, 756, 143964. doi:10.1016/j.scitotenv.2020.143964
[13] Mustafa, A., Kazmi, M., Khan, H. R., Qazi, S. A., & Lodi, S. H. (2022). Towards a carbon neutral and sustainable campus: case study of NED University of Engineering and Technology. Sustainability, 14(2), 794. doi:10.3390/su14020794
[14] Cano, N., Berrio, L., Carvajal, E., & Arango, S. (2022). Assessing the carbon footprint of a Colombian university campus using the UNE-ISO 14064–1 and WRI/WBCSD GHG Protocol Corporate Standard. Environmental Science and Pollution Research. doi:10.1007/s11356-022-22119-4
[15] Osorio, A. M., Úsuga, L. F., Vásquez, R. E., Nieto-Londoño, C., Rinaudo, M. E., Martínez, J. A., & Leal Filho, W. (2022). Towards carbon neutrality in higher education institutions: case of two private universities in Colombia. Sustainability, 14(3), 1774. doi:10.3390/su14031774
[16] Battistini, R., Passarini, F., Marrollo, R., Lantieri, C., Simone, A., & Vignali, V. (2023). How to assess the carbon footprint of a large university? The case study of University of Bologna’s multicampus organization. Energies, 16(1), 166. doi:10.3390/en16010166
Notes: References 10 to 19 are universities that measured their footprint.

## Slide 32: Universities, schools and Egypt
REFERENCES · 3 OF 5
[17] Ahonen, V. L., Woszczek, A., Baumeister, S., Helimo, U. T., Jackson, A. K., Kopsakangas-Savolainen, M., Kääriä, J., Lehtonen, T., Luoranen, M., Pongrácz, E., Soukka, R., Vainio, V., & El Geneidy, S. (2024). Carbon neutral higher education institutions: a reality check, challenges and solutions. International Journal of Sustainability in Higher Education, 25(9), 293–315. doi:10.1108/IJSHE-11-2023-0515
[18] Rus, T., Moldovan, R.-P., Beu, D., Pop, M., & Ceclan, A. (2025). Towards a climate-neutral campus: carbon footprint assessment in higher education institutions. Applied Sciences, 15(7), 3695. doi:10.3390/app15073695
[19] Yang, C., Yao, T., Dong, S., & Jiang, W. (2025). Carbon emissions accounting and uncertainty analysis in campus settings: a case study of a university in Sichuan, China. PLOS ONE. doi:10.1371/journal.pone.0321216
[20] Wagner, O., Tholen, L., Nawothnig, L., & Albert-Seifried, S. (2021). Making school-based GHG-emissions tangible by student-led carbon footprint assessment program. Energies, 14(24), 8558. doi:10.3390/en14248558
[21] Adhikari and Pokhrel (2025). Study on the carbon footprint of schools in Pokhara, Nepal. Himalayan Journal of Applied Science and Engineering, 5(2), 173–183. doi:10.3126/hijase.v5i2.74787
[22] Badr, M. K., El Beheary, M., & Hassan, I. A. (2026). The importance of calculating the carbon footprint of Egyptian universities and their role in sustainable development: Port Said University as case study. Annals of the Academy of Romanian Scientists, Series on Biological Sciences. doi:10.56082/annalsarscibio.2026.1.191
[23] Safwat, H., Abdel-Rehim, A. A., El-Mahallawi, I., Hussein, A. A., Amer, A. M., Elshazly, E., & Elshamy, A. I. (2024). Guidelines for data collection on energy performance of higher-education buildings in Egypt: a case study. HBRC Journal, 20(1), 615–642. doi:10.1080/16874048.2024.2345553
[24] Hamada, A. A., Hong, S.-M., & Raslan, R. (2025). Evaluating the operational performance in Cairo’s public administrative buildings: stock characterisation and typical energy use. Energy and Buildings, 346, 116065. doi:10.1016/j.enbuild.2025.116065
Notes: References 20 and 21 are schools; 22 to 24 are Egyptian studies.

## Slide 33: Monitoring, targets, apps and transport
REFERENCES · 4 OF 5
[25] García-Monge, M., Zalba, B., Casas, R., Cano, E., Guillén-Lambea, S., López-Mesa, B., & Martínez, I. (2023). Is IoT monitoring key to improve building energy efficiency? Case study of a smart campus in Spain. Energy and Buildings, 285, 112882. doi:10.1016/j.enbuild.2023.112882
[26] Akenji, L., Bengtsson, M., Toivio, V., Lettenmeier, M., et al. (2021). 1.5-Degree Lifestyles: Towards a fair consumption space for all. Hot or Cool Institute, Berlin.
[27] Crippa, M., Guizzardi, D., Pagani, F., et al. (2024). GHG emissions of all world countries: 2024 report. Publications Office of the European Union, Luxembourg. JRC138862. doi:10.2760/4002897
[28] Ajufo, C., & Bekaroo, G. (2021). An automated personal carbon footprint calculator for estimating carbon emissions from transportation use. In Proceedings of the International Conference on Artificial Intelligence and its Applications (icARTi ’21). ACM. doi:10.1145/3487923.3487935
[29] Bekaroo, G., Roopowa, D., Zakari, A., & Niemeier, D. (2021). Calculating carbon emissions from personal travelling: insights from a top-down analysis of key calculators. Environmental Science and Pollution Research, 28(7), 8853–8872. doi:10.1007/s11356-020-11179-z
[30] Zhang, Y., Echchabi, O., Feng, T., Zhang, W., Liao, H.-K., & Chang, C. (2026). Detecting transportation mode using dense smartphone GPS trajectories and Transformer models. International Journal of Geographical Information Science. arXiv:2603.00340
[31] Sadeghian, P., Håkansson, J., & Zhao, X. (2021). Review and evaluation of methods in transport mode detection based on GPS tracking data. Journal of Traffic and Transportation Engineering (English Edition), 8(4), 467–482.
[32] Wang, L., Gjoreski, H., Ciliberto, M., Lago, P., Murao, K., Okita, T., & Roggen, D. (2021). Three-year review of the 2018–2020 SHL challenge on transportation and locomotion mode recognition from mobile sensors. Frontiers in Computer Science, 3, 713719. doi:10.3389/fcomp.2021.713719
Notes: Reference 25 is continuous IoT monitoring on a campus; 26 and 27 give the targets and country data; 28 to 33 are personal footprint apps and transport mode detection.

## Slide 34: Food, energy, forecasting and data
REFERENCES · 5 OF 5
[33] Wang, P., & Jiang, Y. (2022). Transportation mode detection using temporal convolutional networks based on sensors integrated into smartphones. Sensors, 22(17), 6712. doi:10.3390/s22176712
[34] Tahir, G. A., & Loo, C. K. (2021). A comprehensive survey of image-based food recognition and volume estimation methods for dietary assessment. Healthcare, 9(12), 1676. doi:10.3390/healthcare9121676
[35] Dalakleidi, K. V., Papadelli, M., Kapolos, I., & Papadimitriou, K. (2022). Applying image-based food-recognition systems on dietary assessment: a systematic review. Advances in Nutrition, 13(6), 2590–2619. doi:10.1093/advances/nmac078
[36] Ismail, M. L., & Sahari, N. (2024). Real time energy monitoring & current spikes detection system for enhanced energy conservation in residential area. Progress in Engineering Application and Technology, 5(1), 79–87. doi:10.30880/peat.2024.05.01.008
[37] Miller, C., et al. (2020). The ASHRAE Great Energy Predictor III competition: overview and results. Science and Technology for the Built Environment, 26(10). doi:10.1080/23744731.2020.1795514
[38] Anand, P., Deb, C., Yang, K., Yang, J., Cheong, D., & Sekhar, C. (2021). Occupancy-based energy consumption modelling using machine learning algorithms for institutional buildings. Energy and Buildings, 111478. doi:10.1016/j.enbuild.2021.111478
[39] Himeur, Y., Ghanem, K., Alsalemi, A., Bensaali, F., & Amira, A. (2021). Artificial intelligence based anomaly detection of energy consumption in buildings: a review, current trends and new perspectives. Applied Energy, 287, 116601. doi:10.1016/j.apenergy.2021.116601
[40] Azad, Rajabi and Estebsari (2023). Non-intrusive load monitoring (NILM) using deep neural networks: a review. arXiv:2306.05017
Data: Miller et al. (2020), Building Data Genome 2, Scientific Data 7:368; Kelly & Knottenbelt (2015), UK-DALE, Scientific Data 2:150007; Bossard et al. (2014), Food-101, ECCV. Factors: Poore & Nemecek (2018), Science 360:987–992; Low-Carbon Power, Egypt (2024); UK DESNZ (2024).
Notes: Food recognition: 34 and 35. Energy monitoring, forecasting and waste: 36 to 40.

## Slide 35: Thank you
BASMATI · بصمتي
Questions and feedback
Notes: Close by repeating what we need to start: approval of the pilot on the CS floor, the official letter for installation, access to the timetable and bills, and the consent form for 20 volunteers.